## Slide 1: Module 2 - Systems
MIS5122: Enterprise Architecture for IT Auditors

## Slide 2: Agenda
Systems Topics
  Central Processing Unit (CPU)
    Control Unit
    Arithmetic Logic Unit (ALU)
    Registers
  The System Bus
    I/O Basics
  Processing Parallelism
    Multicore Processing
    Scaling up & out
Class Activity
  Building our own computer

## Slide 3: Case Study – Focus on Systems
Desktops
Servers
Special Purpose Machines NAS Routers

## Slide 4: Question?
Is a 2.4 GHz Xeon twice as fast as a 1.2 GHz Pentium III?
Is a 3.4 GHz Xeon twice as fast as a 1.7 GHz Xeon?
Will my program run in half the time on the 3.4 GHz Xeon vs. the 1.7 GHz Xeon?
Notes: Remember: Speed is determined by many factors? What factors?

## Slide 5
Notes: Control unit
Moves data and instructions between main memory and registers
Tells the ALU what to do
Arithmetic logic unit (ALU)
Performs computation and comparison operations
All input and output to registers
Set of registers
Storage locations that hold inputs and outputs for the ALU

## Slide 6: How a Microprocessor Works

## Slide 7: Registers
What are “general-purpose” registers?
What are “special-purpose” registers?
Notes:     General Purpose Registers - Hold data for currently executing program that is needed quickly or frequently
Hold intermediate results and frequently needed data items
Used only by currently executing program
Implemented within the CPU; contents can be read or written quickly
Increasing their number usually decreases program execution time to a point
Special Purpose Registers - Store information about currently executing program and about status of CPU
Track processor and program status
Types
  Instruction register
  Instruction pointer
  Program status word (PSW)
    Stores results of comparison operation
    Controls conditional branch execution
    Indicates actual or potential error conditions

## Slide 8: Word Size
What is the “word size” of a machine?
Notes: Word Size
Number of bits a CPU can process simultaneously
Increasing it usually increases CPU efficiency, up to a point
Other computer components should match or exceed it for optimal performance
  CPU components (ALU, registers), bus, RAM, etc.
Implications for system bus design and physical implementation of memory

## Slide 10: What did you learn?
A(n) _______ is the number of bits processed by the CPU in a single instruction. It also describes the size of a single register.
The address of the next instruction to be fetched by the CPU is held in the _______________.
word
instruction pointer

## Slide 11: What did you learn?
In many CPUs, a register called the _____ stores condition codes, including those representing processing errors and the results of comparison operations.
PSW

## Slide 12: Clock Rate
What is the “clock rate” of a machine?
How is it typically measured?
What is the CPU cycle time?
What are “wait states”?
Notes: Typically measured in thousands of MHz (1000 MHz = 1 GHz)
CPU cycle time – inverse of clock rate
  Can typically fetch and execute simple instruction in 1 cycle
Rate of actual or average instruction execution is measured in MIPS or MFLOPS
Wait state
  Waiting to access memory
  Waiting to access I/O devices

## Slide 13: What did you learn?
The _________ time of a processor is 1 divided by the clock rate (in Hz).
One ______ is one cycle per second.
cycle time
hertz

## Slide 14: Question?
In your own words, what does Moore’s law have to do with making CPUs faster?

## Slide 15: The Physical CPU
Electrical device implemented as silicon-based microprocessor
Contains millions of switches, which perform basic processing functions
Physical implementation of switches and circuits

## Slide 16: Why binary?
What is the “decimal” system and why do we use it?
How would we count if we had four fingers on each hand?
Binary is just another numbering system, no better or worse than decimal
  Use binary numbers to represent numeric values
  Use binary numbers to represent characters
Favorite saying
  “There are 10 types of people in this world, those who understand binary and those who don’t”
It’s cheap and easy to make circuits that deal with two and only two voltages
  High voltage represents a 1
  Low voltage represents a 0

## Slide 17: Switches and Gates
What are “switches” and “gates”?
Notes: Basic building blocks of computer processing circuits
Electronic switches
  Control electrical current flow in a circuit
  Implemented as transistors
Gates
  An interconnection of switches
  A circuit that can perform a processing function on an individual binary electrical signal, or bit

## Slide 18
Not
And
Or
XOr
NAnd

## Slide 19
XOr
XOr
XOr
XOr
And
And
And
A | B | Carry | Sum
0 | 0 | 0 | 0
1 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 1 | 1 | 0

## Slide 20
Look at the physical length of the circuit and we’re only adding a pair of 6 bit numbers. How long would the circuit be if we were multiplying a pair of 32 bit numbers or 64 bit numbers?

## Slide 21: Electrical Properties Affect speed and reliability of CPU
Conductivity | Ability of an element to enable electron flow
Resistance | Loss of electrical power that occurs within a conductor
Heat | Negative effects of heat: Physical damage to conductor Changes to inherent resistance of conductor Dissipate heat with a heat sink
Speed and circuit length | Time required to perform a processing operation is a function of length of circuit and speed of light (approx 186,000 miles per second) Reduce circuit length for faster processing

## Slide 22
Moore’s Law - Rate of increase in transistor density on microchips doubles every 18-24 months with no increase in unit cost

## Slide 23: What did you learn?
___________ predicts that transistor density and processor power will double every two years or less.
Moore’s law

## Slide 24: Case Study – The Fastest CPUs?
Servers
A few special purpose desktops?

## Slide 25
The System Bus
Notes: System Bus (FSB)
Connects CPU with main memory and peripheral devices
Set of data lines, control lines, and status lines
  Data bus
  Address bus
  Control bus
Bus protocol
  Number and use of lines
  Procedures for controlling access to the bus

## Slide 26: The System Bus

## Slide 27: Question?
If I have one system with an 800 MHz bus and another system with a 1.6 GHz bus, will the second system run application twice as fast as the first system?

## Slide 28
Load R1,1000
1000
Read from RAM
And wait for 1 bus cycle
127.34
Address | Data | 
1000 | 127.34 | Subtotal
1001 | 0.07 | Tax rate
1002 |  | Tax
Register | Value
R1 | 
R2 | 
127.34

## Slide 29
Load R2,1001
1001
Read from RAM
And wait for 1 bus cycle
0.07
Address | Data | 
1000 | 127.34 | Subtotal
1001 | 0.07 | Tax rate
1002 |  | Tax
Register | Value
R1 | 
R2 | 
127.34
0.07

## Slide 30
Multiply R1,R2
And wait for 1 clock cycle
Address | Data | 
1000 | 127.34 | Subtotal
1001 | 0.07 | Tax rate
1002 |  | Tax
Register | Value
R1 | 
R2 | 
127.34
0.07
8.91

## Slide 31
Store R2,1002
1002
Store into RAM
And wait for 1 bus cycle
8.91
Address | Data | 
1000 | 127.34 | Subtotal
1001 | 0.07 | Tax rate
1002 |  | Tax
Register | Value
R1 | 
R2 | 
127.34
8.91
8.91

## Slide 32: Bus Clock and Data Transfer Rate
What is the “bus clock pulse” and a “bus cycle”?
What do these have to do with “data transfer rate”?
Notes: Bus clock pulse
  Common timing reference for all attached devices
  Frequency measured in MHz
Bus cycle
  Time interval from one clock pulse to the next
Data transfer rate
  Measure of communication capacity
  Bus capacity = data transfer unit x clock rate

## Slide 33: Case Study – The Fastest FSBs?
Servers
A few special purpose desktops?

## Slide 34: What did you learn?
The ___________ is the communication channel that connects all computer system components.
The system bus can be decomposed logically into three sets of transmission lines: the _______bus, the ________ bus, and the ____ bus.
system bus
address
control
data

## Slide 35: Question?
What does it mean when I say that a device controller insulates the system from the physical geometry of I/O devices?
How do device controllers insulate the system from the physical geometry of I/O devices?

## Slide 36: Logical Access – I/O Ports
What is meant by “logical access” and how do “I/O ports” facilitate logical access?
Notes: Communication pathway from CPU to/from peripheral device
Usually a memory address that can be read/written by the CPU and a single peripheral device
Also a logical abstraction that enables CPU and bus to interact with each peripheral device as if the device were a storage device with linear address space
Mailbox analogy

## Slide 37
Logical access: The device, or its controller, translates linear sector address into corresponding physical sector location on a specific track and platter.

## Slide 38
Notes: Device Controller
Used by secondary storage and I/O devices
Implement the bus interface and access protocols
Translate logical addresses into physical addresses
Enable several devices to share access to a bus connection

## Slide 39: What did you learn?
A(n) ________ is a memory address to which the CPU copies data when writing to an I/O or storage device.
The operating system normally views any storage device as a(n) _________________, thus ignoring the device's physical storage organization.
I/O port
Linear address space

## Slide 40: What did you learn?
Part of the function of a storage secondary device controller is to translate _______________ into physical addresses.
logical addresses

## Slide 41: Question?
What are the big differences between buffers and caches?

## Slide 42: Buffers and Caches
What is a “buffer” and what is a “cache”? How are they similar? How are they different?
Notes: Improve overall computer system performance by employing RAM to overcome mismatches in data transfer rate and data transfer unit size
A buffer is a region of memory used to temporarily hold data while it is being moved from one place to another within a computer.while a cache is a temporary storage area where frequently accessed data can be stored for rapid access.

## Slide 43
Notes: Buffer
Mailman/mailbox analogy
Small storage areas (usually DRAM or SRAM) that hold data in transit from one device to another
Use interrupts to enable devices with different data transfer rates and unit sizes to efficiently coordinate data transfer
Buffer overflow

## Slide 44
Intel Itanium® 2 microprocessor uses three levels of primary storage caching.
Can limit wait states by using SRAM cached between CPU and SDRAM primary storage:
Level one (L1): within CPU
Level two (L2): on-chip
Level three (L3): off-chip
Notes: Cache
Differs from buffer:
  Data content not automatically removed as used
  Used for bidirectional data
  Used only for storage device accesses
  Usually much larger
  Content must be managed intelligently
Achieves performance improvements differently for read and write accesses

## Slide 45: Case Study – The Largest Caches?
Servers
A few special purpose desktops?

## Slide 46: What did you learn?
A(n) _______ is a small area of memory used to resolve differences in data transfer rate or data transfer unit size.
A(n) ______ is an area of fast memory where data held on a storage device is prefetched in anticipation of future requests for that data.
buffer
cache

## Slide 47: What did you learn?
A(n) ____ cache is implemented on the same chip as the CPU and is integrated into the same circuitry as the CPU.
L1

## Slide 48: Processing Parallelism
Increases computer system computational capacity; breaks problems into pieces and solves each piece in parallel with separate CPUs
Techniques
  Multicore processors
  Multi-CPU architecture
  Clustering

## Slide 49: Question?
What type of system is faster?
  A 4-way system with four separate CPUs
  A quad-core system

## Slide 50
Notes: Multicore Processors
Include multiple CPUs and shared memory cache in a single microchip
Typically share memory cache, memory interface, and off-chip I/O circuitry among the cores
Reduce total transistor count and cost and provide synergistic benefits

## Slide 51: Case Study – Multiple Processors or Multicore Processors?
Servers
A few special purpose desktops?

## Slide 52: Multi-CPU Architecture
Employs multiple single or multicore processors sharing main memory and the system bus within a single motherboard or computer system
Common in midrange computers, mainframe computers, and supercomputers
Cost-effective for
  Single system that executes many different application programs and services
  Workstations

## Slide 53: Scaling Up
What is “scaling up”?
Notes: Increasing processing by using larger and more powerful computers
Used to be most cost-effective
Still cost-effective when maximal computer power is required and flexibility is not as important

## Slide 54: Scaling Out
What is “scaling out”?
Notes: Partitioning processing among multiple systems
Speed of communication networks; diminished relative performance penalty
Economies of scale have lowered costs
Distributed organizational structures emphasize flexibility
Improved software for managing multiprocessor configurations

## Slide 55: Computer System Classes
Microcomputer | Meets information processing needs of single user Examples: PCs, network computers
Portable | Meets information processing needs of a single user at a variety of levels Examples: laptop, network, PDA
Midrange computer | Supports many programs and users simultaneously
Mainframe | Handles information processing needs of large number of users and applications Large amounts of data storage and access
Supercomputer | Designed for rapid mathematical computation

## Slide 56
Table 2.2 Representative products in various computer classes (2009)

## Slide 57: Multicomputer Configurations
Any organization of multiple computers to support a specific set of services or applications
Common configurations
  Cluster
  Blade
  Grid
  Cloud

## Slide 58: Cluster
Group of similar or identical computers that cooperate to provide services or execute a common application
  Connected by high-speed network
  Typically located close to one another
Advantages: scalability and fault tolerance
Disadvantages: complex configuration and administration

## Slide 59: Blade
Circuit board that contains most of a server
Same advantages and disadvantages as a cluster, but also:
  Concentrate more computing power in less space
  Are simpler to modify

## Slide 60: Grid
Group of dissimilar computer systems, connected by high-speed network, that cooperate to provide services or execute a common application
Computers may be in separate rooms, buildings, or continents
Computers work cooperatively at some times, independently at others

## Slide 61: Cloud
Set of computing resources with two components:
  Front-end interfaces
  Back-end resources
Specific way of organizing computing resources for maximum availability and accessibility
Minimum complexity in the user or service interface

## Slide 62: Case Study – Focus on Systems
Desktops
Servers
Special Purpose Machines NAS Routers

## Slide 63: Review
Systems Topics
  Central Processing Unit (CPU)
    Control Unit
    Arithmetic Logic Unit (ALU)
    Registers
  The System Bus
    I/O Basics
  Processing Parallelism
    Multicore Processing
    Scaling up & out