## Slide 1: Intro to Ethical Hacking
MIS 5211.001
Week 2
Site: http://community.mis.temple.edu/itacs5211fall16/

## Slide 2: Conference Opportunity
BSides 2016 in Delaware
  October 7-8
Link: http://www.bsidesdelaware.com/registration/
Past presentations are available on YouTube: http://www.youtube.com/user/BSidesDE

## Slide 3: Questions From Students
Categories
  Please use them
  Category titles have been corrected. For future posts please select the appropriate category.

## Slide 4: Tonight's Plan
Cyber Crime Laws
Network Components and their impact on penetration testing
Linux fundamentals (Will not cover in class, review if you need it)

## Slide 5: Cyber Crime Laws
Computer Fraud and Abuse Act (1030)
  Obtaining National Security Information
  Accessing a Computer and Obtaining Information
  Trespassing in a Government Computer
  Accessing to Defraud and Obtain Value
  Damaging a Computer or Information
  Trafficking in Passwords
  Threatening to Damage a Computer
  Attempt and Conspiracy

## Slide 6: Cyber Crime Laws
Wiretap Act (2511)
Unlawful Access to Stored Communication (2701)
Identity Theft (1028)
Access Device Fraud (1029)
CAN-SPAM Act (1037)
Wire Fraud (1343)
Communication Interference (1362)
Source: Prosecuting Computer Crimes
http://www.justice.gov/criminal/cybercrime/docs/ccmanual.pdf

## Slide 7: Cyber Crime Laws
Electronic Communications Privacy Act (2510)
  Makes intercepting cell phones illegal
Cyber Security Enhancement Act of 2002 (145)
  Life in prison if cause or attempt to cause a death
  An amendment to USA Patriot Act

## Slide 8: Sate Cyber Crime Laws
Many (Most) states have their own laws
In PA
  Tit. 18 §7601
  Misdemeanor - Unlawful transmission of e-mail is misdemeanor of 3rd degree; unless causes damage of $2,500 or more, then misdemeanor of 1st degree.
  Felony - Unlawful use, disruption of service, theft, unlawful duplication, trespass and distribution of virus are felonies of 3rd degree
Source: http://criminallaw.uslegal.com/cyber-crimes/

## Slide 9: International Cyber Crime Laws
Penetration testers need to comply with applicable laws in:
  Country they are working in
  Country or Countries the systems targeted are located in
  Country or Countries they traverse
If any of the above take you out of the US, need to contact an appropriate lawyer.

## Slide 10: Questions
?

## Slide 11: Networking
The very first internetworked connection:
Source: http://en.wikipedia.org/wiki/Internet_protocol_suite

## Slide 12: Networking
Today
Source: http://www.cisco.com/c/en/us/td/docs/solutions/Enterprise/Data_Center/ServerFarmSec_2-1/ServSecDC/2_Topolo.html

## Slide 13: Internet Protocol Suite
How Data fits together:

## Slide 14: A word about Ports
Ports – logical assignment to packets of data
Used to distinguish between different services that run over transport protocols such as TCP and UDP
IANA Registry:
http://www.iana.org/assignments/service-names-port-numbers/service-names-port-numbers.xhtml?&page=1

## Slide 15: Protocols
What we will cover
  IP
  ICMP
  UDP
  TCP
  ARP

## Slide 16: IP Protocol
Internet Protocol
  Primary protocol of the Internet Layer of the Internet protocol
  Three main functions
    For outgoing packets – Select the next hop host (Gateway)
    For incoming packets – Capture the packet and pass up the protocol stack as appropriate
    Error detection

## Slide 17: IP Protocol
Source: http://nmap.org/book/tcpip-ref.html

## Slide 18: ICMP Protocol
Internet Control Message Protocol
  Used by network devices to communicate status
  Not “typically” used to exchange data
  Does not have a “port” assignment
  Not usually accessed by end-users accept for:
    ping
    traceroute

## Slide 19: ICMP Protocol
Source: http://nmap.org/book/tcpip-ref.html

## Slide 20: UDP Protocol
User Datagram Protocol
  Simple transmission model with limited mechanisms
  No guarantee of delivery
  No acknowledgement of receipt
  Does include checksum and port numbers

## Slide 21: UDP Protocol
Source: http://nmap.org/book/tcpip-ref.html

## Slide 22: TCP Protocol
Transmission Control Protocol
  Sometimes called TCP/IP
  Provides reliable, ordered and error checked delivery of a stream of data (or Octets) across local area networks, intranets, and public internet
This is the protocol used for HTTP, HTTPS, SMTP, POP3, IMAP, SSH, FTP, Telnet, and others

## Slide 23: TCP Protocol
Source: http://nmap.org/book/tcpip-ref.html

## Slide 24: ARP Protocol
Address Resolution Protocol
  Used to convert an IP address to a MAC Address
  MAC Address is the unique hardware address written into the hardware of every network card
    Example: 6C-62-6D-05-F9-18
    Tells me my Network Card comes from Micro-Star INTL CO., LTD in Taiwan (based on 6C-62-6D)
  Can be altered by software

## Slide 25: Network Components
Switches
Routers
Firewalls
  Standard
  Next Generation
  Web Application
Load Balancers
Proxies
Reverse Proxies
DNS

## Slide 26: Switches
Used to connect devices together on a network
Depending on functionality can operate at different layers of the OSI model
  “Layer 1” – Hub – Traffic is not managed – Every packet repeated to every port
  “Layer 2” – Data Link Layer – Some management – Switch knows MAC Address of locally connected devices and sends appropriate packets
  “Layer 3” – Switch understands “routing” and knows what packets to pass out of the local segment
Microsoft Explanation of OSI Model : http://technet.microsoft.com/en-us/library/cc959881.aspx

## Slide 27: Routers
Forwards packets between computer networks
Works to keep localized traffic inside and only passes traffic intended for targets outside the local network
Boundary between “Routable” and “Non-Routable” IP addressing

## Slide 28: Non-Routable Addressing (Private)
10.0.0.0 to 10.255.255.255
  Class A
  16,777,216 addresses
172.16.0.0 to 172.31.255.255
  Class B
  1,048,576 addresses
192.168.0.0 to 192.168.255.255
  Class C
  65,536 addresses

## Slide 29: Firewalls (Standard)
Standard Enterprise Firewalls are “2nd Generation”, implies stateful
Filters traffic based on:
  Address
  Port
Stateful: Retains enough data about previous packets to understand connection state

## Slide 30: Firewalls (Next Generation)
Extend operation into the Application layer
Provides for Application layer filtering
  Understands certain applications and protocols
  Can determine if data inside a packet is consistent with the application or protocol

## Slide 31: Firewalls (Web Application)
Similar to Next Generation, but retains even more information around “normal” web site activity
Builds a profile of how users interact with a website, and what the traffic should look like
Generates alerts when patterns change
Can generate false positives if web site undergoes high volumes of change

## Slide 32: Network Address Translation (NAT)
Modifies network addresses in the IP datagram
Translation – Replaces the IP address in the packet with another address
  Obscures addressing behind the NAT device, typically a firewall
  Can convert non-routable addresses to routable addresses
  Means the address you see is not necessarily the address of the target device

## Slide 33: Load Balancers
Distributes sessions across multiple server
  User does not “Know” what server is in use
  May terminate SSL connection for server, improving server performance
    May apply additional SSL restrictions outside of certification rules
  Internal tester can usually direct access to a particular machine or cell via alternate port

## Slide 34: Proxies
Intermediary between client machines and the rest of the network or internet
Can function as a NAT device
May be an embedded function of a firewall or may be stand alone
Uses
  Content filtering
  Logging and/or monitoring
  Can obfuscate internal network details

## Slide 35: Reverse Proxies
Similar to proxy, but typically sits in front of servers
Uses
  Hides details of server infrastructure
  Can perform SSL termination function
  Can reduce server load by caching
Can be embedded in a load balancer or firewall, or may be a stand-alone device

## Slide 36: DNS
Domain Name System
  Consists of a tree of domain names
  Example
    Root -> .edu -> temple.edu
Basically the phone book for the internet

## Slide 37: Servers
Examples
  File
  Web
  Application
  Database
  Log

## Slide 38: Typical Web Arrangement

## Slide 39: Security Technologies
Intrusion Detection Systems (IDS)
Intrusion Prevention Systems (IPS)
Network Behavioral Anomaly Detection (NBAD)
Data Loss Prevention (DLP)
Host Intrusion Detection (HIDS)
Host Intrusion Prevention (HIPS)
Baseline and Host File Integrity

## Slide 40: IDS and IPS
Analyzes packets and matches to known signatures to either alert or block traffic
Basically a burglar alarm for the network

## Slide 41: NBAD
Network Flow Analysis
Flow is metadata about network traffic passing through the infrastructure
System profiles “Normal” behavior and alerts on deviation from normal

## Slide 42: DLP
Monitors for activity against “sensitive” data.
Can be on servers and hosts
Can be on network
Typically knows what confidential or personally identifiable information PII looks like
  Format of Social Security Numbers
  Format of account numbers
  Key words like Confidential, Account, etc…

## Slide 43: HIDS and HIPS
Similar to IDS and IPS, but resides on individual servers or workstations
Augments AV software
Can generate a lot of noise
Can interfere with Scanning and Penetration Testing

## Slide 44: Baseline and Host File Integrity
Establishes a baseline configuration for servers and monitors for deviation
Develops signature for key files on systems and monitors for change
Can help ensure systems stay configured as desired.
Last line of defense to detect compromise of a system.

## Slide 45: Questions
?

## Slide 46: Next Week
Reconnasaince
Meeting at Temple, Alter 603

## Slide 47: Linux
What is Linux
  Open source operating system
  Many similarities with UNIX
Why do we care
  Some tools only available in Linux
  Some tools work better in Linux
  Best open source attack suites are built on Linux
    Kali
    Samurai WTF (Web Testing Framework)
    SIFT (SANS Investigative Forensic Toolkit)

## Slide 48: Logging In
For Kali the default password is toor
For Samurai the default password is samurai

## Slide 49: root
“root” is the base admin account on a Linux system.
Should not be used for routine operations

## Slide 50: SUDO
Used to execute commands that require root privilege
Requires user to supply their password, not the root password

## Slide 51: Changing Passwords (passwd)
“passwd” command is used to change passwords
Any user can change their password by typing passwd at the command prompt.
Will be prompted to enter new password twice
“root” or sudo user can change others passwords with command:
  passwd [login_name]

## Slide 52: Changing Accounts
“su” command allows you to jump to another user account (with appropriate password of course)
“whoami” command tells you who you are logged in as

## Slide 53: Linux File System

## Slide 54: Navigating File System
Command cd [directory_name] changes directory
Command cd.. Moves up one level
Command pwd tells you were you are
Command cd by itself takes you to your home directory

## Slide 55: Viewing Directories
Command ls lists directory content
Flags
  -l – details including permissions
  -a – shows all files
When in doubt use command “man ls”, this gives you the manual or man page for the command

## Slide 56: Output from ls -la

## Slide 57: Make and Remove Directories
Command mkdir creates directory
As before man mkdir gives you the manual
Command rmdir removes directory

## Slide 58: Make and Remove Directories

## Slide 59: Locate and Find
Command locate checks an index on system to look for common items
Command find searches file system
On my test implementation, find required sudo privileges

## Slide 60: Locate and Find

## Slide 61: Editing Files
Lots of choices, lets keep it simple
Command gedit opens a text editor
Command gedit test opens an existing file named test. If no such file exists, the file is created
Edit as wish, save when done

## Slide 62: Editing Files

## Slide 63: Viewing Files
Command cat shows content of a file

## Slide 64: Looking at Output
Output often larger then screen
Commands less and more
Work similarly
  less requires you hit q when done to return to command prompt
  more dumps to command prompt when last screen is completed

## Slide 65: Miscellaneous Commands
Command ps shows running processes
  Lots of switches to refine results
Command CTRL-z interrupts running com
Command bg restores interrupted command to run in background
Command & tells job to run in background from the beginning
Command jobs shows jobs running
Command fg moves job to foreground

## Slide 66: Network
Command ifconfig shows network configuration. Similar to ipconfig in windows

## Slide 67: Netstat
Netstat prints information about the Linux networking subsystem. The type of information printed is controlled by the first argument, as follows:
  (none) – By default, netstat displays a list of open sockets. If you don't specify any address families, then the active sockets of all configured address families will be printed.
  --route , -r – Display the kernel routing tables. See the description in route(8) for details. netstat -r and route -e produce the same output.
  --groups , -g – Display multicast group membership information for IPv4 and IPv6.
  --interfaces, -I – Display a table of all network interfaces.
  --masquerade , -M – Display a list of masqueraded connections.
  --statistics , -s – Display summary statistics for each protocol.

## Slide 68: Netstat

## Slide 69: grep
grep searches the named input FILEs for lines containing a match to the given PATTERN. By default, grep prints the matching

## Slide 70: Grep w/ netstat and ps
Try grep with netstat to see what is using http
netstat -nap | grep http
Try grep with ps to see if cron is running
ps aux | grep cron

## Slide 71: Grep w/ netstat and ps

## Slide 72: Going Further
Get VMWare and a Linux ISO
  Kali
  http://www.kali.org/downloads/
  Ubuntu
  http://www.ubuntu.com/download/desktop
Give it a try
All examples here where created in a clean, plain vanilla Ubuntu install