## Slide 1: Intro to Ethical Hacking
MIS 5211.001
Week 7
Site: http://community.mis.temple.edu/mis5211sec001f14/

## Slide 2: Tonight's Plan
Mid-Term
In the news
NetCat

## Slide 3: In The News
Submitted
  http://www.cnet.com/news/at-t-warns-1600-customers-of-data-breach/

## Slide 4: In The News
What I noted
  http://www.securityweek.com/hackers-compromised-yahoo-servers-using-shellshock-bug
  http://www.datacenterdynamics.com/focus/archive/2014/10/stromasys-emulates-legacy-hardware-cloud
  http://the-digital-reader.com/2014/10/06/adobe-spying-users-collecting-data-ebook-libraries/#.VDS-f3l0yUl
  http://krebsonsecurity.com/2014/10/huge-data-leak-at-largest-u-s-bond-insurer/
  http://www.dailydot.com/politics/gmail-tor-lockout-problem/

## Slide 5: Netcat
Netcat is a utility used by Penetration Tester and Hackers to establish network connections over UDP or TCP.
Takes “Standard In”, and sends it across the network as data
Receives network data and puts it on “Standard Out”
Messages from netcat itself go on “Standard Error”

## Slide 6: A Word About stdin, stdout, and stderror
These are terms from programming that refer to expected streams in software
As an example
  stdin would be the keyboard
  Stdout would be the screen
  Stderror may be dropped or sent to logging
From: http://en.wikipedia.org/wiki/Standard_streams#Standard_error_.28stderr.29

## Slide 7: Netcat in Linux and Windows
In Linux netcat is typically installed and can be activate simply by typing “nc” at the command line
In Windows, the file is not installed
  A version can be downloaded from:
    http://nmap.org/ncat/
  Once downloaded and extracted type “ncat” at the command line to get started
  Note – AV will likely automatically remove it

## Slide 8: Simple Demo

## Slide 9: Netcat Structure
Basic format is
  Send
    $nc [Target IP] [Remote Port]
  Receive
    $nc [flag(s)] [Local Port]
  Assumes TCP unless –u flag is set forcing to UDP
Link to SANS Cheat Sheet
  URL: http://www.sans.org/security-resources/sec560/netcat_cheat_sheet_v1.pdf

## Slide 10: Pipes
So, netcat can send what I type to another machine. So what!
The pipe commands “|”, “>”, and “<“ let you do more interesting things
For example, transfer a file between systems
  $nc –l –p [Local Port] > [Out File]
    Listen on local port and store result in file
  $nc –w3 [TargetIP] [Port] < [In File]
    Push file to target IP on port
See SANS Cheat Sheet on previous page for more examples

## Slide 11: Port Scanning
You can even use netcat as a simple port scanner
Example
  $nc –v –n –z –w1 [Target IP] [Starting Port] – [Ending Port]
  Systematically attempts to connect on each port within the defined range
  Note:
    -v – Verbose
    -n – Do not resolve names
    -z – Do not send data
    -w1 – Wait no more then one second to connect

## Slide 12: Next Week
2nd formal assignment
From Syllabus
  (student presentations) (student presentations) Scanning exercise targeted against only systems you personally own, develop a profile of the targeted machine or machines. You may work in teams, or separately
    One to two page Executive Summary
    Short (no more then three slides, no welcome slide) presentation
    See “Exercise Analysis” tab for more details

## Slide 13: Next Week
Readings and Articles as usual
We will be covering
  Social Engineering
  Encoding
  Encryption

## Slide 14: Questions
?