## Slide 1: Intro to Ethical Hacking
MIS 5211.701
Week 12

## Slide 2: Tonight's Plan
BSides DE
Introduction to Wireless Security
Next Week

## Slide 3: Wireless Security
First, a small bit of trivia:
Who invented the technology we now think of as WiFi?

## Slide 4: The Answer
  Source: http://www.pixmule.com/hedy-lamarr/ and https://en.wikipedia.org/wiki/Hedy_Lamarr#/media/File:Lamarr_patent.png
The Actress Hedy Lamar

## Slide 5: Security vs Mobility
Wireless is different
  Physical security is no longer relevant
    Access from outside perimeter
    Users connecting to “other” networks
  Users and Networks are vulnerable even when not in use

## Slide 6: More Issues
Attack tools are cheap
  Hardware is close to zero
  Software is zero
Segregation doesn’t work
  Even with “guest” networks, there still on your wires and can still cause you issues
Fallacy of “We don’t have any wireless”
  No, you just don’t know about the wireless you have

## Slide 7: Still More Issues
Encryption doesn’t protect you, at least not completely
Authentication doesn’t protect you, at least not completely
Firewalls? Really, we’re going to go their?
Why would anybody attack us?

## Slide 8: Leakage
Signal required to use wireless access means you need to be relatively close
Signal required to “sniff” traffic means attacker could be miles away with the right conditions
Source: http://www.engadget.com/2007/06/19/venezuelans-set-new-wifi-distance-record-237-miles/

## Slide 9: Old Ways Are The Worst Ways
Wireless networking is a shared segment
  Think “Hub”, not “Switch”
Sniffing is passive
  No access required
  No forensic evidence attacker was there
  Only need some level of physical proximity
So, you would need to be here, to be safe. Maybe!
Source: http://www.darkgovernment.com/news/wp-content/uploads/2009/04/area-51-satellite-image.jpg

## Slide 10: Denial of Service
RF Jamming
  Expensive
  Traceable
802.11 attacks
  Cheap (Free?)
  Can look like regular traffic
  Effective, and hard to locate

## Slide 11: Protocol Issues
Long history of problems
  WEP
  LEAP
  Bluetooth authentication
  Preferred networks broadcast
  Management frames cannot be encrypted
    Easily captured
  Geo Location

## Slide 12: Standards
Multiple players
  FCC – Federal Communications Commission
  IEEE – Institute of Electrical and Electronics Engineers
  IETF – Internet Engineering Task Force
  WiFi Alliance

## Slide 13: FCC
Government Regulatory Body
  Sets output power limits
  Investigates interference cases
  Requires acceptance testing of new products prior to going on sale
  Covers all of US including territories

## Slide 14: IEEE
Develops the detailed “specifications” for layer 1 and 2
  PHY
  MAC
Complies with FCC and other country regulatory bodies
Membership made up of vendors, manufactures, etc…

## Slide 15: IETF
Similar makeup to IEEE
Responsible for layer 3 and above
Standards are published as RFCs

## Slide 16: WiFi Alliance
Trade Organization
Focused on interoperability
In early days, worked out pre-specification requirements due to vendor concerns over time required by IEEE and IETF

## Slide 17: EAP
Extensible Authentication Protocol
Defines framework to authenticate users to the network (Not limited to Wireless)
Works with IEEE 802.1x
IETF provides extremely detailed information
  http://tools.ietf.org/html/rfc3748

## Slide 18: 802.11i
The replacement for WEP
Provided for enhanced security
Introduces TKIP and CCMP
  TKIP – Temporal Key Interchange Protocol
  CCMP - Counter Mode Cipher Block Chaining Message Authentication Code Protocol, Counter Mode CBC-MAC Protocol or simply CCMP
Later rolled in to 802.11-2007

## Slide 19: 802.11 MAC Layer
Definitions
  “dB” – Decibels
  SSID – Service Set Identifier (Name Advertised)
  BSSID – Basic Service Set Identifier (Think MAC Address)
  EAP Extensible Authentication Protocol
  EAPOL – EAP over LAN

## Slide 20: 802.11 MAC Layer
Basic access mechanism
Fragmentation support
Reliable data delivery
Network separation on same frequency (BSSID)
Mobility between BSSs (Roaming)
Power Management

## Slide 21: Architectures
Not just Access Points
  Peer to Peer (Ad-Hoc)
  Point to Point (Typically proprietary to bridge locations where cabling is not feasible, also known as Wireless Distribution Networks)
  Mesh (Think massive ad-hoc)
  Wireless Switches

## Slide 22: 802.1x
IEEE Specification for network authentication
Originally designed for wired networks
Used for NAC (Network Access Control)
Requires
  Supplicant (End point agent)
  Authenticator (Typically a 802.1x capable switch)
  Authentication Server (LDAP, AD, etc…)

## Slide 23: 802.11 Framing
802.11-2007 defines MAC layer
Three types of frames
  Management (Beacon, Probe, Authentication)
  Data
  Control (Confirmation of packet reception)
Defines addressing and features
Designed to accommodate roaming, power management

## Slide 24: More Wireless Security
Open WiFi Networks vs Encrypted WiFi Networks
  In an open network, your browsing can be monitored
  Every thing is sent in the clear
  WPA2-PSK fixes this “Somewhat”

## Slide 25: WPA2-PSK
Uses a pre-shared key (hence the acronym PSK)
  The pre-shared key is known to all authorized users
  Anyone with the pre-shared key has what they need to decrypt traffic
  Wireshark has a built in option to decrypt traffic if you have the key
  This means WPA2-PSK is not much more secure than no encryption, unless you trust everyone on the network

## Slide 26: Wireshark WPA2-PSK Decryption
Edit->Preferences->IEEE 802.11

## Slide 27: PTK or Pairwise Transient Key
WPA2-PSK tries to address this issue by use of PTK
However, the PTK is derived from the PSK
So… It is easy to capture the PTK if you have the PSK

## Slide 28: WPA2-Enterprise
WPA2-Enterprise corrects these issues for large networks
  EAP authentication along with a Radius server ensures each client gets a unique key
  Other authenticated users no longer have a master key to decrypt the traffic

## Slide 29: WPA2 Hole196 Vulnerability
Even in WPA2-Enterprise there is still a potential vulnerability from other authorized users (Abuses GTK or Group Temporal Key)
Limited to:
  ARP poisoning
  Injecting malicious code
  Denial of Service w/o using de-auth packets
More detailed description
  https://community.arubanetworks.com/t5/Community-Tribal-Knowledge-Base/Analysis-of-quot-Hole-196-quot-WPA2-Attack/ta-p/25382

## Slide 30: Key Reinstallation Attack
Also known as KRACK
The attack works against all modern protected Wi-Fi networks
https://www.krackattacks.com
Basically takes advantage of weakness in protocol to reinstall keys

## Slide 31: Kismet
802.11 wireless:
  Network detector
  Sniffer
  Intrusion detection system
Works with any wireless card which supports raw monitoring mode (not all do)
Can sniff:
  802.11b
  802.11a
  802.11g
  802.11n

## Slide 32: Kismet
Supports a plugin architecture allowing for additional non-802.11 protocols to be decoded
Identifies networks by passively collecting packets and detecting networks, which allows it to detect (and given time, expose the names of) hidden networks and the presence of non-beaconing networks via data traffic

## Slide 33: Kismet in Kali
Pre-installed in Kali
Did not launch from drop down menu in my instance
Needed to start from command line
Be patient, it will walk through configuration
You can automate via configuration files, but for now just follow prompts

## Slide 34: Getting Started
We will
  Get USB Wireless Adapter working with Kali
  Launch and configure Kismet
  Explore a little bit

## Slide 35: Connecting Wireless Card

## Slide 36: Checking Card
Use the command: iwconfig
This should give something like the following:

## Slide 37: Kismet
Kismet is a wireless network detector, sniffer, and intrusion detection system. Kismet works predominately with Wi-Fi (IEEE 802.11) networks, but can be expanded via plug-ins to handle other network types.
Features
  802.11 sniffing
  Standard PCAP logging (compatible with Wireshark, TCPDump, etc)
  Client/Server modular architecture
  Plug-in architecture to expand core features
  Multiple capture source support
  Live export of packets to other tools via tun/tap virtual interfaces
  Distributed remote sniffing via light-weight remote capture
  XML output for integration with other tools
http://kismetwireless.net/

## Slide 38: Starting Kismet

## Slide 39: Kismet Example

## Slide 40: Wireshark
Pre-installed in Kali

## Slide 41: Wireshark

## Slide 42: Or

## Slide 43: Startup of Wireshark
Will throw an error due to running as root in Kali, just click OK and move on
Will need to turn wireless menu on by going to View tab and clicking on “Wireless Toolbar”

## Slide 44: Configuring Interface
Select “wlan0mon”
Click on “Start”
Be patient, it will take a minute or so to update

## Slide 45: More Wireshark

## Slide 46: Questions
?