## Slide 1: Advanced Penetration testing
MIS 5212.001
Week 9
Site: http://community.mis.temple.edu/mis5212sec001sp2017/

## Slide 2: Tonight's Plan
Introduction to Wireless Security
Next Week

## Slide 3: Wireless Security
First, a small bit of trivia:
Who invented the technology we now think of as WiFi?

## Slide 4: The Answer
  Source: http://www.pixmule.com/hedy-lamarr/ and https://en.wikipedia.org/wiki/Hedy_Lamarr#/media/File:Lamarr_patent.png
The Actress Hedy Lamar

## Slide 5: Security vs Mobility
Wireless is different
  Physical security is no longer relevant
    Access from outside perimeter
    Users connecting to “other” networks
  Users and Networks are vulnerable even when not in use

## Slide 6: More Issues
Attack tools are cheap
  Hardware is close to zero
  Software is zero
Segregation doesn’t work
  Even with “guest” networks, there still on your wires and can still cause you issues
Fallacy of “We don’t have any wireless”
  No, you just don’t know about the wireless you have

## Slide 7: Still More Issues
Encryption doesn’t protect you, at least not completely
Authentication doesn’t protect you, at least not completely
Firewalls? Really, we’re going to go their?
Why would anybody attack us?

## Slide 8: Leakage
Signal required to use wireless access means you need to be relatively close
Signal required to “sniff” traffic means attacker could be miles away with the right conditions
Source: http://www.engadget.com/2007/06/19/venezuelans-set-new-wifi-distance-record-237-miles/

## Slide 9: Old Ways Are The Worst Ways
Wireless networking is a shared segment
  Think “Hub”, not “Switch”
Sniffing is passive
  No access required
  No forensic evidence attacker was there
  Only need some level of physical proximity
So, you would need to be here, to be safe. Maybe!
Source: http://www.darkgovernment.com/news/wp-content/uploads/2009/04/area-51-satellite-image.jpg

## Slide 10: Denial of Service
RF Jamming
  Expensive
  Traceable
802.11 attacks
  Cheap (Free?)
  Can look like regular traffic
  Effective, and hard to locate

## Slide 11: Protocol Issues
Long history of problems
  WEP
  LEAP
  Bluetooth authentication
  Preferred networks broadcast
  Management frames cannot be encrypted
    Easily capture
  Geo Location

## Slide 12: Standards
Multiple players
  FCC – Federal Communications Commission
  IEEE – Institute of Electrical and Electronics Engineers
  IETF – Internet Engineering Task Force
  WiFi Alliance

## Slide 13: FCC
Government Regulatory Body
  Sets output power limits
  Investigates interference cases
  Requires acceptance testing of new products prior to going on sale
  Covers all of US including territories

## Slide 14: IEEE
Develops the detailed “specifications” for layer 1 and 2
  PHY
  MAC
Complies with FCC and other country regulatory bodies
Membership made up of vendors, manufactures, etc…

## Slide 15: IETF
Similar makeup to IEEE
Responsible for layer 3 and above
Standards are published as RFCs

## Slide 16: WiFi Alliance
Trade Organization
Focused on interoperability
In early days, worked out pre-specification requirements due to vendor concerns over time required by IEEE and IETF

## Slide 17: EAP
Extensible Authentication Protocol
Defines framework to authenticate users to the network (Not limited to Wireless)
Works with IEEE 802.1x
IETF provides extremely detailed information
  http://tools.ietf.org/html/rfc3748

## Slide 18: 802.11i
The replacement for WEP
Provided for enhanced security
Introduces TKIP and CCMP
  TKIP – Temporal Key Interchange Protocol
  CCMP - Counter Mode Cipher Block Chaining Message Authentication Code Protocol, Counter Mode CBC-MAC Protocol or simply CCMP
Later rolled in to 802.11-2007

## Slide 19: 802.11 MAC Layer
Definitions
  “dB” – Decibels
  SSID – Service Set Identifier (Name Advertised)
  BSSID – Basic Service Set Identifier (Think MAC Address)
  EAP Extensible Authentication Protocol
  EAPOL – EAP over LAN

## Slide 20: 802.11 MAC Layer
Basic access mechanism
Fragmentation support
Reliable data delivery
Network separation on same frequency (BSSID)
Mobility between BSSs (Roaming)
Power Management

## Slide 21: Architectures
Not just Access Points
  Peer to Peer (Ad-Hoc)
  Point to Point (Typically proprietary to bridge locations where cabling is not feasible, also known as Wireless Distribution Networks)
  Mesh (Think massive ad-hoc)
  Wireless Switches

## Slide 22: 802.1x
IEEE Specification for network authentication
Originally designed for wired networks
Used for NAC (Network Access Control)
Requires
  Supplicant (End point agent)
  Authenticator (Typically a 802.1x capable switch)
  Authentication Server (LDAP, AD, etc…)

## Slide 23: 802.11 Framing
802.11-2007 defines MAC layer
Three types of frames
  Management (Beacon, Probe, Authentication)
  Data
  Control (Confirmation of packet reception)
Defines addressing and features
Designed to accommodate roaming, power management

## Slide 24: Next Week
More wireless
  Kismet
  More about WEP
  Intro to AirCrack

## Slide 25: Questions
?